## Slide 1
MX dialect: typed IR to RV64
FP4 GEMM → typed MX
%acc = "mx_gemmini.contract"(%A,%As,%B,%Bs) {
activation_format = "fp4_e2m1",
weight_format = "fp4_e2m1", pe_mode = 0 : i32 }
%out = "mx_gemmini.readout_bf16"(%acc)
resource → packed codes + E8M0 scales → mvin; contract → MX compute. Radiance softmax uses vpu_execute; readout_bf16 / spad_requant / wait finish the tile.
Compiled attention object → binary
__asm__ volatile(
".insn r 0x7b, 3, 2, x0, %0, %1"
: : "r"(Q_IN),
"r"(0x0010001000000000));
objdump: 4a: 04b6b07b .insn 4, 0x04b6b07b
physical_program orders mvin → compute → VPU → mvout. RoCC C + data asm → RV64 GCC → ELF → Nicolas Spike.
Implemented transforms and checks
bind_profile
Legal PE tuple +
profile digest
MXBF16Catalog
Preparation
Select BF16
MX sites
schedule.plan
Choose native
loop policy
MXVPUPostOffload
Map softmax, add
and reductions
physical_program
Order DMA, compute
and VPU commands
mx-gemmini-opt verifies typed IR. The standalone command path bypasses LLVM; the generic full-model host currently uses Merlin → LLVM → RV64.
01 / 03
Notes: System block diagram
Replace the sample content with your project information. Diagram roles and measurements on style pages are template conventions, not research claims.

## Slide 2
One JSON profile changes legal MLIR
Selected RTL profile fields
{
"geometry": {"mesh_rows":16,"mesh_columns":16},
"legal_compute": [
{"activation_format":"fp4_e2m1",
"weight_format":"fp4_e2m1","pe_mode":0},
{"activation_format":"fp8_e4m3",
"weight_format":"fp8_e4m3","pe_mode":8}
],
"resources": {"scratchpad_bytes":262144,
"vpu":true,"spad_requant":true}
}
MxE4M3Fp4VpuGemminiRocketConfig · direct projections in both legal rows · two 8-lane BF16 VPUs.
RTL 266c593 + MxGen dba3e7 → 41 fragments / 40 SoC wrappers; each JSON stores source hashes.
Before → after bind_profile
before: contract {format = "mxfp4"}
after: contract {
activation_format = "fp4_e2m1",
weight_format = "fp4_e2m1",
pe_mode = 0 : i32,
profile_sha256 = "e9e33f..." }
Compiler consequences
• TinyLlama: 155 FP4 / 45 FP8 MX sites per stage.
• FP4 binds PE 0; 256 KiB SPAD caps tiles.
• VPU/requant legal; FP6 rejects in this profile.
• load_profile(profile, rtl_root=rtl) rejects drift.
npu-exploration supplies source kernels for per-mode Spike checks; the RTL profile alone is structural, not a performance claim.
02 / 03
Notes: Five-stage process
Replace the sample content with your project information. Diagram roles and measurements on style pages are template conventions, not research claims.

## Slide 3
Spike cycles by comparison scope
Workload / compared code | Compiler cycles | Nicolas path cycles | Compiler Δ
SmolVLA full 12 steps · issuer swap | 72,066,544,354* | 71,875,683,634 | +0.266%
TinyLlama full 33 steps · issuer swap | 83,547,564,353* | 83,544,602,795 | +0.004%
SmolVLA flow 1 step · issuer swap | 2,112,653,481 | 2,112,919,925 | −0.0126%
Dense attention 64×256×128 · fused source | 43,523 | 43,641 | −0.27%
* Output hashes match: SmolVLA 33/33; TinyLlama 99/99. This checks the captured outputs, not model accuracy.
Nicolas e4m3_vpu Spike, host tracking off. The dense attention row compares one fused kernel, not a whole model.
Full-model rows change only the MX matrix command code. Both runs use the same Merlin host and VPU code.
Nicolas's fused MX+VPU kernels have not yet been stitched and timed as either complete model.
03 / 03
Notes: Results table
Replace the sample content with your project information. Diagram roles and measurements on style pages are template conventions, not research claims.